## Slide 1: From Outer Space to Sub Surface: Seismic vibrations, how to measure them, and the impact of COVID19 lockdown
Artash Nath
Grade 8 Student
Twitter: @wonrobot www.HotPopRobot.com
Artash.Nath@gmail.com
Royal Astronomical Society of Canada, Toronto,
15 July 2020

## Slide 2: Seismic Vibrations Tell Stories!
Geology of Planets
Interior structure, tectonic plate movements, volcanoes
Weather Phenomena
Wind and dust storms
Meteor Strikes
Human Activities
Transport, mining, rocket launches

## Slide 3: Seismometers: To Measure Seismic Vibrations
Simple Pendulum with a heavy mass!
3 separate pendulums to record displacement along 3 axis:
north-south
east-west
up-down
Inverted Pendulum: for more sensitivity
up-down
east-west / north-south
inverted pendulum designs

## Slide 4: Astronomy: Are Seismic Vibrations desirable or undesirable?
Both
Desirable to understand Planetary Geology
Undesirable to detect Gravitational Waves: Laser Interferometer Gravitational-Wave Observatory (LIGO)
In both cases we make use of Pendulums!
Check out my previous 2019 RASC Toronto talk on how LIGO uses Quadruple Pendulums to eliminate seismic vibrations

## Slide 5: Moon: Apollo Missions (1969-1972)
Apollo Missions 11, 12, 14, 15, 16 carried seismometers
Readings came until 1977
Apollo 11 seismometer lasted only ~3 weeks.
Apollo 17 carried a Gravimeter: to measure difference in the force of gravity from one place to another
Image Credit: https://agupubs.onlinelibrary.wiley.com/doi/full/10.1002/2014JE004724

## Slide 6: Lunar Quakes: Causes + Data
Causes:
Tidal Forces: Gravitational forces exerted by Earth
Global Contraction: Moon is shrinking as its interior cools
Data (between 1969 and 1977)
28 shallow moonquakes, ranging from magnitude 1.5 to 5.0 on the Richter scale
> 1700 meteoroid impacts (almost 1 per day) with impactor masses between 0.5 and 5000 kilograms

## Slide 7
Third stages of several Saturn V rockets, and Ascent stages of lunar modules were deliberately crashed into the Moon.
Produced seismic events of known times and locations - helped to calibrate the network of seismometers.
Artificial Lunar Quakes Observed
Seismometer readings from Apollo 17 Saturn S-IVB impacting the Lunar surface arrive at NASA
Image Credit: https://en.wikipedia.org/wiki/Lunar_seismology

## Slide 8: Mars: Viking Lander Missions (1976)
Viking 1 seismometer did not get activated
Viking 2 seismometer operated for 500+ sols
Seismometers mounted on top bay. Affected by Wind Noise + lander’s equipment activity
Only one event (on Sol 80) was considered as possible seismic event. But upper limits to seismic vibrations were calculated
seismometer
Image Credit: https://www.drewexmachina.com/2018/11/21/viking-the-first-seismometers-on-mars/

## Slide 9: First Likely Mars Quake Heard by NASA InSight (April 6, 2019, the 128th Martian day, or sol, of the mission)
https://mars.nasa.gov/news/8430/nasas-insight-detects-first-likely-quake-on-mars/?site=insight

## Slide 10: Mars: NASA Insight (2018)
Landed in the Elysium Planitia region of Mars on 26 Nov 2018.
SEIS (Seismic Experiment for Interior Structure):
the round, dome-shaped instrument
2 Sets of Seismometers:
3 axis Very Broad Band (VBB) sensors:
0.01-10 Hz frequency bandwidth (Main Instrument)
3 axis Short Period (SP) sensors:
0.1-50 Hz frequency bandwidth (for Redundancy)

## Slide 11: Mars Quakes Causes + Data
Causes:
Global Contraction: Constant internal cooling process, which happens inside most rocky planets
Data (through 30 September 2019): 174 events
24 events (magnitude 3 – 4) propagating from as far down as the planet’s mantle
150 small-magnitude events occurring frequently and propagating from the crust (wind, landslides, unsure)
Mars quakes resemble more closely to those of moon quakes than earthquakes

## Slide 12: Seismic Vibrations on Earth
Train Signal
Cruise Ship Signal
Wind Signal
Mining / Explosion
Human Activities

## Slide 13: Earthquake Signals
Signals become very strong in very short time
These may be aftershocks
P, S, Surface Waves from the same earthquake that have travelled in different ways and at different speeds
Several stations register the signal
Source: https://earthquake.usgs.gov/learn/glossary/?term=S%20wave

## Slide 14: Quakes: Earth vs. Mars vs Moon
Earthquakes: Larger magnitudes, Shorter duration
Moon + Mars quakes: Longer duration. Smaller magnitudes
Earthquakes release lot more energy than Moon and Mars quakes

## Slide 15: Using Seismic Vibrations to Study Impact of COVID19 Lockdown on Canadian Cities
Calgary, AB Edmonton, AB
Montreal, QC Ottawa, ON
Toronto, ON Yellowknife, NWT
https://softwareunderground.org/

## Slide 16: Data Source Data Type
Data files type:
MiniSEED (MSEED) containing Waveform data
Python library:
ObsPy to download and process MSEED files
http://ds.iris.edu/ds/nodes/dmc/data/

## Slide 17: Raw Data Processing – Overlapping and Averaging
Chart: Average Displacement (every 15 minutes) with 50% overlap. Toronto
Chart: Average Displacement (Daily) Toronto
The RMS (average displacement) was calculated for each 15-minute period inside the main Probabilistic Power Spectral Densities (PPSD) files, with an overlap of 50%. The same is done for each 24-hour period in the data
Followed tutorial by Thomas Lecocq (github.com/ThomasLecocq/SeismoRMS) on visualizing and plotting seismic data over time
9,486,720,000‬ lines of seismic data used for Analysis
Chart: Average Seismic Displacement (Averaged for every 2 weeks)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 9.13e-09 | 1.2096e-08 | 1.8294e-08 | 9.7514e-09 | 1.1767e-08 | 1.2544e-08 | 9.9857e-09 | 1.0934e-08 | 8.3086e-09 | 1.067e-08 | 4.3108e-09 | 5.4723e-09 | 3.2985e-09
To Analyse the Trend

## Slide 18: Calgary, AB
Chart: Averaged Seismic Displacement in Calgary (Dec 2019 – June 2020)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 9.9057e-10 | 5.1029e-10 | 9.3529e-10 | 2.3673e-09 | 2.2859e-09 | 2.5035e-09 | 2.5953e-09 | 1.6637e-09 | 9.4331e-10 | 1.2503e-09 | 2.0329e-09 | 1.8385e-09 | 2.3085e-09
State of Emergency: 15 March 2020
31% decrease in seismic vibrations after lockdown
Network: CN
Station: TD022
Channel: HHZ
Location: --

## Slide 19: Edmonton, AB
Chart: Averaged Seismic Displacement in Edmonton (Dec 2019 – June 2020)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 1.8541e-09 | 1.9189e-09 | 1.9106e-09 | 1.9656e-09 | 1.9168e-09 | 1.8459e-09 | 1.7019e-09 | 1.6385e-09 | 1.8382e-09 | 1.4831e-09 | 1.368e-09 | 1.2756e-09 | 1.3898e-09
Network: CN
Station: TD002
Channel: HHZ
Location: --
State of Emergency: 15 March 2020
14% decrease in seismic vibrations after lockdown

## Slide 20: Montreal, QC
Chart: Average Seismic Displacement in Montreal (Dec 2019 – June 2020)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 7.97e-10 | 7.97e-10 | 8.16e-10 | 8.5e-10 | 8.3e-10 | 9.11e-10 | 9.09e-10 | 7.6e-10 | 7.07e-10 | 7.57e-10 | 8.8e-10 | 9.13e-10 | 9.09e-10
State of Emergency: 27 March 2020
34 % decrease in seismic vibrations after lockdown
Network: CN
Station: MNTQ
Channel: HHZ
Location: --

## Slide 21: Ottawa, ON
Chart: Average Daily Seismic Displacement in Ottawa (Dec 2019 – June 2020)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 9.2614e-10 | 9.3471e-10 | 1.1894e-09 | 1.1904e-09 | 1.0364e-09 | 1.0551e-09 | 1.0729e-09 | 1.0989e-09 | 1.0879e-09 | 1.1584e-09 | 1.3369e-09 | 1.1634e-09 | 1.1401e-09
State of Emergency: 25 March 2020
8% increase in seismic vibrations after lockdown
Network: CN
Station: OTT
Channel: HHZ
Location: --

## Slide 22: Yellowknife, NWT
Chart: Average Daily Seismic Displacement in Yellowknife (Dec 2019 – June 2020)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 4.217e-11 | 4.1551e-11 | 3.9889e-11 | 5.4466e-11 | 6.3801e-11 | 6.1784e-11 | 6.2091e-11 | 4.9797e-11 | 2.7425e-11 | 2.8894e-11 | 2.9159e-11 | 3.4e-11 | 3.389e-11
State of Emergency: 24 March 2020
44 % decrease in seismic vibrations after lockdown
Network: CN
Station: YKAW1
Channel: HHZ
Location: --

## Slide 23: Toronto, ON
Chart: Averaged Seismic Displacement in Toronto (Dec 2019 – June 2020)
| 43814 | 43828 | 43842 | 43856 | 43870 | 43884 | 43898 | 43912 | 43926 | 43940 | 43954 | 43968 | 43982
Average Seismic Vibation | 9.13e-09 | 1.2096e-08 | 1.8294e-08 | 9.7514e-09 | 1.1767e-08 | 1.2544e-08 | 9.9857e-09 | 1.0934e-08 | 8.3086e-09 | 1.067e-08 | 4.3108e-09 | 5.4723e-09 | 3.2985e-09
State of Emergency: 23 March 2020
34 % decrease in seismic vibrations after lockdown
Network: CN
Station: TORO
Channel: HHZ
Location: --

## Slide 24: LIVE DEMO: Raspberry Shake Community Seismic Network
My Toronto Seismic Station using Raspberry Shake https://raspberryshake.net/stationview/#?net=AM&sta=RC893

## Slide 25: My Online Training Module: Do It Yourself Seismic Analysis
GitHub : Artash-N
https://github.com/Artash-N/COVID19-Impact-on-Seismic-Activity
Join Software Underground Community: Place for scientists that like rocks and computers. https://softwareunderground.org/

## Slide 26: From Outer Space to Sub Surface: Seismic vibrations, how to measure them, and the impact of COVID19 lockdown
Artash Nath
Grade 8 Student
Twitter: @wonrobot www.HotPopRobot.com
Artash.Nath@gmail.com
Royal Astronomical Society of Canada, Toronto,
15 July 2020